## Slide 2
Energy scenario construction for a village
Jyrki Luukkanen, Mika Korkeakoski
Research Director
Finland Futures Research Centre
jyrki.luukkanen@utu.fi
DEEM training

## Slide 3: Village electricity use How to construct a scenario
What are the factors which affect the electricity use?
How these factors can be assessed?
What are the important factors from the point of view of electricity system planning?
How the factors may change in the future?

## Slide 4: Electricity system planning
Different programmes available for electricity system planning
HOMER is a system for small scale village level system planning
To be able to use the planning models you have to know about the electricity demand and different aspects related to it (like load curve)

## Slide 5: Electricity demand
Factors affecting the demand:
  Size of the village
  Number of households
    Household is usually seen as the energy consuming unit
  Household activities that need electricity
    Equipment and their properties
    How long they are used (per day)
  Industrial activities (carpenter, rice miller, etc.)
  Service activities (cafe, hairdresser, school, health center, etc.)

## Slide 6: Electricity system properties
Electricity supply must always match the consumption
Production must be controlled to equal the demand in order to keep the frequency and voltage at constant level (not to damage devices)
Demand varies considerable during the day, week and season

## Slide 7: Electricity demand in Finland in one week

## Slide 8: Load curve for a group of villages in Cambodia
Chart: Load curve for group of villages
| 0-1 | 1-2 | 2-3 | 3-4 | 4-5 | 5-6 | 6-7 | 7-8 | 8-9 | 9-10 | 10-11 | 11-12 | 12-13 | 13-14 | 14-15 | 15-16 | 16-17 | 17-18 | 18-19 | 19-20 | 20-21 | 21-22 | 22-23 | 23-24
 | 40 | 40 | 40 | 40 | 40 | 50 | 50 | 50 | 50 | 60 | 60 | 60 | 60 | 60 | 60 | 50 | 50 | 100 | 100 | 130 | 130 | 130 | 40 | 40

## Slide 9: Load curve for a small village
Chart: Load curve for a small village
| 0-1 | 1-2 | 2-3 | 3-4 | 4-5 | 5-6 | 6-7 | 7-8 | 8-9 | 9-10 | 10-11 | 11-12 | 12-13 | 13-14 | 14-15 | 15-16 | 16-17 | 17-18 | 18-19 | 19-20 | 20-21 | 21-22 | 22-23 | 23-24
 | 0 | 0 | 0 | 0 | 0.2 | 3 | 0.3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.2 | 6 | 11 | 12 | 9 | 3 | 0.3

## Slide 10: Factors affecting investment planning
Peak load (highest demand in kW) and its duration
Base load or lowest demand and its duration
The load duration curve (LDC) is used in electric power generation to illustrate the relationship between generating capacity requirements and capacity utilization

## Slide 11: Load duration curve
A load duration curve illustrates the variation of a certain load in a downward form such that the greatest load is plotted in the left and the smallest one in the right. On the time axis, the time duration for which each certain load continues during the day is given

## Slide 12: How to get information of electricity demand
Make assumptions of household (and other) consumption
If the electrification is in the planning phase you have to make assumptions (no data exists), but you can get information of already electrified villages
Carry out a survey, where energy use is asked in detail (survey will be discussed in next lectures)

## Slide 13: Excel based calculation of potential electricity demand

## Slide 14: Simple results
Chart: 
| 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0 | 2033.0 | 2034.0 | 2035.0 | 2036.0
Annual electr cons. MWh, lamps | 2.044 | 2.147 | 2.2552 | 2.3689 | 2.4883 | 2.6137 | 2.7454 | 2.8838 | 3.0291 | 3.1818 | 3.3422 | 3.5106 | 3.6875 | 3.8734 | 4.0686 | 4.2737 | 4.4891 | 4.7153 | 4.953 | 5.2026 | 5.4648 | 5.7402 | 6.0295
Chart: 
| 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0 | 2033.0 | 2034.0 | 2035.0 | 2036.0
Power demand kW, lamps | 1.4 | 1.4706 | 1.5447 | 1.6225 | 1.7043 | 1.7902 | 1.8804 | 1.9752 | 2.0747 | 2.1793 | 2.2892 | 2.4045 | 2.5257 | 2.653 | 2.7867 | 2.9272 | 3.0747 | 3.2297 | 3.3924 | 3.5634 | 3.743 | 3.9317 | 4.1298

## Slide 15: Simple results
Chart: Household annual electricity consumption
| 2014.0 | 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0 | 2033.0 | 2034.0 | 2035.0 | 2036.0
Annual electr cons. MWh, lamps | 2.044 | 2.147 | 2.2552 | 2.3689 | 2.4883 | 2.6137 | 2.7454 | 2.8838 | 3.0291 | 3.1818 | 3.3422 | 3.5106 | 3.6875 | 3.8734 | 4.0686 | 4.2737 | 4.4891 | 4.7153 | 4.953 | 5.2026 | 5.4648 | 5.7402 | 6.0295
Annual electr cons. MWh, refridgerators | 3.504 | 3.8929 | 4.3251 | 4.8051 | 5.3385 | 5.9311 | 6.5894 | 7.3209 | 8.1335 | 9.0363 | 10.0393 | 11.1537 | 12.3918 | 13.7672 | 15.2954 | 16.9932 | 18.8794 | 20.9751 | 23.3033 | 25.89 | 28.7637 | 31.9565 | 35.5037
Annual electr. use, MWh, DVD sound system | 0.73 | 0.77416 | 0.821 | 0.87067 | 0.92335 | 0.97921 | 1.0385 | 1.1013 | 1.1679 | 1.2386 | 1.3135 | 1.393 | 1.4772 | 1.5666 | 1.6614 | 1.7619 | 1.8685 | 1.9815 | 2.1014 | 2.2286 | 2.3634 | 2.5064 | 2.658
Annual electr. use, MWh, Television | 2.19 | 2.5437 | 2.9545 | 3.4316 | 3.9859 | 4.6296 | 5.3772 | 6.2457 | 7.2543 | 8.4259 | 9.7867 | 11.3673 | 13.2031 | 15.3354 | 17.812 | 20.6887 | 24.0299 | 27.9107 | 32.4183 | 37.6538 | 43.7349 | 50.7981 | 59.002
Annual electr. use, MWh, computer | 0.365 | 0.40552 | 0.45053 | 0.50054 | 0.5561 | 0.61782 | 0.6864 | 0.76259 | 0.84724 | 0.94128 | 1.0458 | 1.1618 | 1.2908 | 1.4341 | 1.5933 | 1.7701 | 1.9666 | 2.1849 | 2.4274 | 2.6969 | 2.9962 | 3.3288 | 3.6983
Annual electr. use, MWh, Fan | 1.825 | 1.9354 | 2.0525 | 2.1767 | 2.3084 | 2.448 | 2.5961 | 2.7532 | 2.9198 | 3.0964 | 3.2837 | 3.4824 | 3.6931 | 3.9165 | 4.1535 | 4.4048 | 4.6713 | 4.9539 | 5.2536 | 5.5714 | 5.9085 | 6.266 | 6.645
Annual electr. use, MWh, Rice cooker | 5.475 | 5.8062 | 6.1575 | 6.53 | 6.9251 | 7.3441 | 7.7884 | 8.2596 | 8.7593 | 9.2892 | 9.8512 | 10.4472 | 11.0793 | 11.7496 | 12.4604 | 13.2143 | 14.0138 | 14.8616 | 15.7607 | 16.7143 | 17.7255 | 18.7979 | 19.9351

## Slide 16: Household load curve

## Slide 17: Household load curve

## Slide 18: Village service and industrial load curve

## Slide 19: Household, service and industrial electricity load curve in a village

## Slide 20: Village service and industrial load curve

## Slide 21
Household, service and industrial electricity load curve in a village

## Slide 22: Case villages

## Slide 23: Thank you